## Slide 1
Routing· Unit 3
Routing Fundamentals
How Routers Forward Packets
From routing tables to static, RIP and OSPF configuration — with the real Cisco IOS commands at every step.
Static Routes
RIP & OSPF
CLI Labs
R1#
R1(config)# ip route 0.0.0.0 0.0.0.0 192.168.1.1
01
ROUTING FUNDAMENTALS

## Slide 2
01 — THE CORE IDEA
What is Routing?
Routers connect multiple networks and decide, packet by packet, the best path to a destination.
1
Packet Reception
Router receives a packet and inspects the destination IP in the header.
2
Route Lookup
Consults its routing table for the most specific matching route.
3
Packet Forwarding
Sends the packet out the correct interface toward its destination.
EXAMPLE — DELIVERING A PACKET TO 192.168.2.50
Router A — decision logic
Router A# show ip route
C 192.168.2.0/24 is directly connected, GigabitEthernet0/1
! Destination 192.168.2.50 matches 192.168.2.0/24 directly
! Packet is forwarded out GigabitEthernet0/1 -- no next hop needed
02
ROUTING FUNDAMENTALS

## Slide 3
02 — THE ROUTING TABLE
Connected, Static & Dynamic Routes
Every routing table is built from three sources, each with a different administrative trust level.
Connected
Added automatically when an interface is assigned an IP and brought up.
Static
Manually configured by an administrator to define a specific path.
Dynamic
Learned automatically via protocols like RIP, OSPF, EIGRP or BGP.
R1#
R1# show ip route
C 192.168.1.0/24 is directly connected, FastEthernet0/0
S 10.0.0.0/8 [1/0] via 192.168.1.2
O 172.16.0.0/16 [110/2] via 192.168.1.3, GigabitEthernet0/1
! C = Connected S = Static O = OSPF (Dynamic)
03
ROUTING FUNDAMENTALS

## Slide 4
03 — MANUAL CONTROL
Static Routing — Command Anatomy
Precise, predictable paths — ideal for small or stub networks where topology rarely changes.
R1(config)#
R1(config)# ip route 192.168.50.0 255.255.255.0 192.168.1.2
ip route
Command keyword
192.168.50.0
Destination network
255.255.255.0
Subnet mask
192.168.1.2
Next-hop IP address
Static routes stay simple and reliable — but need manual updates whenever the topology changes.
Small networks
Stub networks
Backup / predictable paths
04
ROUTING FUNDAMENTALS

## Slide 5
04 — SPECIAL STATIC ROUTES
Default Routes & Floating Static
Two variations on static routing that handle "everything else" and backup paths.
Default Route
Catches all traffic to unknown destinations — the "gateway of last resort."
R1(config)# ip route 0.0.0.0 0.0.0.0 192.168.1.1
Destination 0.0.0.0/0 matches everything not already in the table — vital for stub networks and internet gateways.
Floating Static
A backup route that only activates when the primary route fails.
R1(config)# ip route 10.0.0.0 255.0.0.0 192.168.1.3 250
Administrative distance 250 is higher than a normal static route (1) — so it only kicks in once the primary path is unavailable.
05
ROUTING FUNDAMENTALS

## Slide 6
05 — DYNAMIC PROTOCOLS
Distance Vector vs. Link State
Two fundamentally different ways routers learn and share topology information automatically.
Feature
Distance Vector
Link State
Examples
RIP, IGRP
OSPF, IS-IS
Info exchange
Periodic updates to neighbors
LSAs flooded to all routers in area
Convergence speed
Slower
Faster
Network size
Small to medium
Large and hierarchical
Resource usage
Lower
Higher
RIP uses hop count (max 15); OSPF uses Dijkstra's shortest-path algorithm over a full topology map.
06
ROUTING FUNDAMENTALS

## Slide 7
06 — DISTANCE VECTOR IN PRACTICE
Configuring RIP
A simple distance-vector protocol, well suited to small networks with a flat topology.
R1(config)#
R1(config)# router rip
R1(config-router)# version 2
R1(config-router)# network 192.168.1.0
HOW RIP PICKS A ROUTE
Metric: hop count
Fewer hops always wins — a 3-hop route beats a 5-hop route.
Max 15 hops
16 is considered unreachable — RIP does not scale to large networks.
Periodic updates
Neighbors exchange their full routing table on a fixed timer.
R1#
R1# show ip route rip
R 172.16.0.0/16 [120/2] via 192.168.1.4
! [120/2] = AD 120, metric 2 hops
07
ROUTING FUNDAMENTALS

## Slide 8
07 — LINK STATE IN PRACTICE
Configuring OSPF
Builds a full topology map and computes the shortest path — scales to large, hierarchical networks.
R1(config)#
R1(config)# router ospf 1
R1(config-router)# network 192.168.1.0 0.0.0.255 area 0
Link-State Advertisements
Routers flood LSAs describing their directly connected links to the whole area.
Dijkstra's Algorithm
Each router independently computes the shortest path to every network.
Areas & Hierarchy
Area 0 is the backbone; other areas connect through it to control LSA flooding.
08
ROUTING FUNDAMENTALS

## Slide 9
08 — TRACING A PACKET
Routing in Action — Hop by Hop
A packet from 192.168.1.10 travels through three routers to reach a server at 10.0.0.20.
Source
192.168.1.10
Router 1
Default gateway
Router 2
Next hop lookup
Router 3
Final hop
Destination
10.0.0.20
Each hop: inspects the destination IP → consults its routing table → forwards out the right interface.
C:\>
C:\> tracert 10.0.0.20
1 2 ms 2 ms 1 ms 192.168.1.1 (Router 1)
2 5 ms 4 ms 5 ms 10.10.10.1 (Router 2)
3 8 ms 7 ms 8 ms 10.10.20.1 (Router 3)
4 9 ms 9 ms 10 ms 10.0.0.20 (Destination)
09
ROUTING FUNDAMENTALS

## Slide 10
09 — HANDS-ON LAB
Configuring Static & Dynamic Routes
The full command sequence for both a static route and an OSPF process, ready to type into a Cisco CLI.
STATIC ROUTE
R1
R1> enable
R1# configure terminal
! Create the static route
R1(config)# ip route 172.16.0.0 255.255.0.0 192.168.1.2
! Save the configuration
R1(config)# end
R1# write memory
DYNAMIC ROUTE (OSPF)
R1
R1> enable
R1# configure terminal
R1(config)# router ospf 1
! Advertise both connected networks
R1(config-router)# network 192.168.1.0 0.0.0.255 area 0
R1(config-router)# network 10.0.0.0 0.255.255.255 area 0
! Verify neighbors
R1(config-router)# end
R1# show ip ospf neighbor
10
ROUTING FUNDAMENTALS

## Slide 11
10 — SUMMARY
Key Takeaways
Best-path decisions
Routers determine the best path for forwarding packets using the routing table.
Three route sources
Connected, static and dynamic routes together populate the routing table.
Static vs. Dynamic
Static offers control; dynamic protocols adapt automatically to change.
Two protocol families
Distance vector (RIP, EIGRP) and link state (OSPF) suit different network sizes.
Administrative Distance
Used to pick the best route when multiple sources offer a path.
Traceroute visualizes it
A simple way to see every hop a packet actually takes.
11
ROUTING FUNDAMENTALS

## Slide 12
CONCLUSION
Every Packet Follows
a Deliberate Path
From a single ip route command to a fully converged OSPF area, routing is the discipline of making — and trusting — the right forwarding decision at every hop.
ip route
The single command behind every static path
router rip / ospf
Enables dynamic route learning between neighbors
show ip route
The command that reveals what a router actually knows
tracert / traceroute
Visualizes the real hop-by-hop journey of a packet
Chapter 7 of 20
Next up: OSPF Protocol — link-state routing in depth
Thank you
12
ROUTING FUNDAMENTALS