## Slide 1
NETWORKING FUNDAMENTALS
The OSI Model
Seven layers that standardized how every device on Earth talks to every other device
L1
Physical
L2
Data Link
L3
Network
L4
Transport
L5
Session
L6
Presentation
L7
Application
ISO / OSI Reference Model · Published 1984

## Slide 2
02
WHAT IT IS
A common language for networks
The Open Systems Interconnection (OSI) model is a conceptual framework that divides network communication into seven abstract layers — giving engineers a shared, standardized way to design interoperable hardware and software, regardless of vendor.
Layered, not protocol-specific
Defines tasks for each layer to accomplish, not the exact protocol — leaving room for innovation.
Traffic moves both ways
Each layer talks only to the layers directly above and below it, in either direction.
Software layers vs. hardware layers
Layers 5–7 govern applications; layers 1–3 govern physical transmission; layer 4 bridges both.
L7
Application
L6
Presentation
L5
Session
L4
Transport
L3
Network
L2
Data Link
L1
Physical
— “What is the OSI model?”

## Slide 3
03
ORIGINS
Where the OSI model came from
A patchwork of proprietary networks in the late 1970s pushed the industry toward one shared standard.
LATE 1970S
Proprietary chaos
Manufacturers build their own networking solutions — systems can't interoperate.
EARLY 1980S
ARPANET & TCP/IP
Both prove networking is possible at scale, but expose the need for a universal model.
1980S
ISO + CCITT convene
The two standards bodies begin work on a vendor-neutral, layered framework.
1984
OSI model published
ISO formally releases the seven-layer reference model still taught today.

## Slide 4
04
THE FRAMEWORK
The seven layers, top to bottom
7
Application
User-facing services
HTTP · FTP · DNS · SMTP
6
Presentation
Translate, encrypt, compress
SSL/TLS · JPEG · MPEG
5
Session
Open, manage, close sessions
RPC · NetBIOS
4
Transport
End-to-end delivery — “the heart of OSI”
TCP · UDP
3
Network
Addressing, routing, forwarding
IPv4 · IPv6 · ICMP
2
Data Link
Node-to-node delivery, MAC addressing
Ethernet · ARP
1
Physical
Raw bit transmission over media
Cables · Wi-Fi · Hubs

## Slide 5
05
LAYERS 5–7
The software layers
Layers 5–7 govern everything sent and received by applications — browsers, email clients, and operating systems.
LAYER 7
Application
Closest to the end user. Provides the protocols software uses to send and receive data.
File transfer to the presentation layer
Authenticates devices for transfer
Enables remote access & directory services
LAYER 6
Presentation
Also called the syntax layer — converts data into a format the application layer can use.
Data translation (e.g. EBCDIC → ASCII)
Encryption & decryption
Compression / decompression
LAYER 5
Session
Opens, manages and cleanly terminates connections — called sessions — between devices.
Manages logon / logoff
Synchronization & checkpoints
Session failure recovery

## Slide 6
06
LAYER 4
Transport: the heart of OSI
The transport layer manages end-to-end delivery of complete messages. It breaks messages from the session layer into segments, then reassembles them in order at the destination.
Service point addressing
Attaches a port address so messages reach the correct process.
Flow control
Matches transmission speed between sender and receiver to prevent overflow.
Multiplexing
Lets multiple applications share the same connection at once.
TWO TYPES OF SERVICE
Connection-oriented
Establish → transfer → terminate. The receiver sends an acknowledgment back for every packet delivered — reliable, but slower.
Connectionless
Data transfer only — no delivery confirmation. Faster, but less reliable than connection-oriented service.

## Slide 7
07
LAYERS 1–3
The hardware layers
Layers 1–3 move data through the network's physical components as it's processed and forwarded.
LAYER 3
Network
Handles data addressing and routing across different networks using IPv4 / IPv6.
Fragments large packets, reassembles them
Traffic control to prevent congestion
Delivery isn't guaranteed at this layer
LAYER 2
Data Link
Manages error-free transfer between devices on the same network via MAC addressing.
Split into LLC and MAC sublayers
ARP converts IP → MAC addresses
Detects & retransmits damaged frames
LAYER 1
Physical
The physical assets — cables, routers, radios — that move raw bits between devices.
Defines bit rate & synchronization
Simplex, half- or full-duplex mode
Bus, star or mesh topology

## Slide 8
08
IN ACTION
Sending one email, seven layers deep
Pressing “send” pushes the message down through every layer on the sender's device, then back up through all seven on the recipient's.
7
Application
Chooses SMTP, hands the message off
6
Presentation
Compresses the message data
5
Session
Opens a communication session
4
Transport
Segments the message for transfer
3
Network
Divides segments into packets
2
Data Link
Breaks packets into frames + MAC address
1
Physical
Sends the bit stream over Wi-Fi
At the recipient's device, the bit stream travels back up through Physical → Data Link → Network → Transport → Session → Presentation → Application, landing in the inbox.

## Slide 9
09
COMPARISON
OSI vs. TCP/IP
TCP/IP condenses OSI's seven conceptual layers into four practical ones — and it's what the real internet runs on.
OSI MODEL — 7 LAYERS
TCP/IP MODEL — 4 LAYERS
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Transport
Internet
Network Access

## Slide 10
10
WHY IT STILL MATTERS
Benefits of the OSI model
Accelerated R&D
Layers can be developed and updated independently, so new technology slots in without overhauling the whole stack.
Streamlined knowledge sharing
A common, decomposable structure makes it easy for teams to conceptualize and discuss a network.
Simplified troubleshooting
When something breaks, teams can isolate the problem to a single layer without disrupting the rest.

## Slide 11
Seven layers. One shared language.
The OSI model may not run the modern internet directly — but it still shapes how every engineer thinks about, builds, and troubleshoots a network.