## Slide 1
NETWORK FUNDAMENTALS
TCP/IP
The protocol suite that quietly runs the entire internet
TCP
Transmission Control Protocol
IP
Internet Protocol
Internet Engineering Task Force (IETF) Standard

## Slide 2
02
TWO PROTOCOLS, ONE JOB
What TCP and IP each do
TCP
Transmission Control Protocol
Organizes data so it can move between a server and client — establishing a connection, breaking data into packets, and guaranteeing it all arrives intact.
Establishes a live connection before sending anything
Breaks large data into smaller, numbered packets
Confirms delivery and resends anything lost or corrupted
IP
Internet Protocol
Defines the address — the IP address — every device needs to send and receive data, and the rules for exchanging packets across networks.
Assigns a unique address to every connected device
Tags each packet with source & destination info
Routes packets across one network or many

## Slide 3
03
WORKING TOGETHER
TCP vs. IP: what's the difference?
They're separate protocols that rely on each other — one finds the address, the other makes sure the message gets there.
IP = the phone number
IP obtains and defines the address — the IP address — of the device data must reach. It's the identifier, not the delivery mechanism.
TCP = the phone call
TCP is responsible for transporting and routing data through the network, making sure it actually reaches the destination IP has defined.
Together, TCP + IP let devices communicate over long distances — transferring data to where it needs to go, as efficiently as possible.

## Slide 4
04
CHOOSING A TRANSPORT
TCP vs. UDP
UDP is TCP's leaner alternative — faster, but with none of the delivery guarantees.
TCP
Reliable
CONNECTION
Established before data flows
ORDERING
Packets sequenced & reassembled
ERROR HANDLING
Detects loss, resends automatically
BEST FOR
Email, web (HTTP), file transfer, SSH
UDP
Fast
CONNECTION
None — sends without signaling first
ORDERING
No sequencing guarantee
ERROR HANDLING
No correction — drops are just dropped
BEST FOR
DNS lookups, VoIP, live streaming

## Slide 5
05
CONNECTION SETUP
The three-way handshake
Before a single byte of real data moves, TCP/IP synchronizes both ends of the connection.
Client
Server
1. SYN
Client requests a connection, proposing an initial sequence number
2. SYN-ACK
Server acknowledges and sends its own sequence number back
3. ACK
Client confirms — the connection is now open on both ends
Only after all three steps complete can multiple TCP socket connections transfer data in both directions at once.

## Slide 6
06
THE MODEL
The four layers of TCP/IP
4
Application
Where users interact — email, browsers, messaging
HTTP · SMTP · IMAP · FTP
3
Transport
Reliable delivery — segments data, numbers packets
TCP · UDP
2
Internet
Addresses & routes packets across networks
IP · ICMP · ARP
1
Data Link
Physical transmission of bits over hardware
Ethernet · Wi-Fi · NIC drivers
Data passes down through all four layers to send, then back up through all four to receive.

## Slide 7
07
LAYER BY LAYER
What each layer actually does
Application
LAYER 4
Programs that need TCP/IP to communicate — combines OSI's session, presentation & application layers.
The level users directly interact with
Covers email, messaging, web browsing
HTTP, SMTP, IMAP, FTP protocols live here
Transport
LAYER 3
Provides a solid, reliable connection — this is where data is divided into numbered packets.
Determines how much data to send, and when
Sends packets error-free and in sequence
Confirms the destination received everything
Internet
LAYER 2
Sends packets from a network and controls their movement to make sure they reach their destination.
IP is the main protocol at this layer
Tags each packet with address information
Chooses the path across networks
Data Link
LAYER 1
Handles the physical act of sending and receiving data — also called the link or network access layer.
Combines OSI's physical + data link layers
Governs NICs, Ethernet cables, Wi-Fi radios
Defines how hardware signals raw data

## Slide 8
08
IN ACTION
An email's journey through TCP/IP
Sending one SMTP email touches every layer twice — once down, once back up at the destination.
Application
SMTP server prepares the outgoing message
Transport
TCP divides the message into numbered packets
Internet
IP layer transports each packet toward the destination
Data Link
Packets go out over the physical network hardware
At the destination, packets are handed back to TCP, reassembled in order, and delivered up through Internet → Transport → Application to the recipient's inbox.
Every packet can take a different route to the destination — TCP/IP reroutes automatically if a path is congested or unavailable.

## Slide 9
09
MODEL COMPARISON
TCP/IP vs. the OSI model
TCP/IP is the practical, four-layer model the internet actually runs on — OSI's seven layers map onto it.
TCP/IP MODEL — 4 LAYERS
OSI MODEL — 7 LAYERS
Application
Presentation
Session
Transport
Network
Data Link
Physical
Application
Transport
Internet
Data Link

## Slide 10
10
SECURITY NOTE
Your packets aren't private by default
TCP/IP was built for delivery, not confidentiality. Anything sent in the clear can be seen or intercepted along the way.
Visible in transit
Data packets sent over TCP/IP can be seen or intercepted as they cross the network.
Public Wi-Fi is the biggest risk
Avoid sending private data over open, unsecured Wi-Fi networks.
Encrypt what matters
A VPN encrypts traffic end-to-end, keeping packet contents unreadable to anyone in between.

## Slide 11
Four layers. One connected world.
TCP handles the reliability. IP handles the address. Together, they move nearly every packet on the internet — quietly, and by default, without encryption.